## Slide 1: Manufacturing Downtime Project Data analysis project
Supervised by: Eng/ Kareem Bakli

## Slide 2: Contents of this Presentation
1. Case Study Story | 6. Dashboard
2. Data Exploration Data | 7. Predictive Maintenance Triggers
3. Business Questions | 8. Recommended Action Plan
4. Data Transformation Ideas | 9. Project Impact
5. Insights | 

## Slide 3: Case Study Story

## Slide 4: Data Analysis Team
Team Leader
Rania Mohamed El-wany
Israa Nagy Mohamed
Mayada Kairy Mohamed
Aya Emad Abd Al-manum
Toka Ahmed El-sayed
Hend Adel Ahmed Wafa

## Slide 5
“And then we started with understanding the metadata, then the business questions, followed by exploring the data, preparing clearing transforming, and finally uncovering actionable insights.”
LatheTech Industries came to us with a challenge: "Our machines are experiencing unexpected breakdowns, which heavily impact productivity and increase costs."
01
Heat & Power Issues
02
High Downtime & Costs
Excessive Tool Wear
Reported Issues
03

## Slide 6
Objective
    Analyze machine failures
    Identify root causes behind downtime
    Build automated Power BI dashboard
    Predict high-risk operating conditions
    Recommend proactive maintenance actions

## Slide 7
Data
Exploration

## Slide 8: Dataset purpose This dataset represents the operating conditions of industrial machines and whether they failed. data used in predictive maintenance: predicting and preventing machine breakdowns before they occur. Number of rows: 10,000 Number of columns: 15 “During data exploration, we found that the dataset contained no null or missing values or duplicates which simplified preprocessing.”
Data Description:

## Slide 9
Numeric
  UDI
  Air temperature [K]
  Process temperature [K]
  Rotational speed [rpm]
  Torque [Nm]
  Tool wear [min]
  Downtime (min)
Binary(0/1 Flags)
  Machine failure
  TWF
  HDF
  PWF
  OSF
  RNF
Text
  Type
Date
  Date
Data Description:
Text
  Type
Date
  Date

## Slide 10
Data dictionary:
Column | Description | Why it matters
UID | Unique identifier for each record. Just a running number. | Used to reference rows, not useful for analysis.
Product ID | Identifies the product being manufactured, including its quality and a variant-specific serial number grade (Low, Medium, High). | Different product qualities may affect wear and failure.
Type | Quality grade of the product: L = Low, M = Medium, H = High. | Higher-quality products may last longer.

## Slide 11
Data dictionary:
Air temperature [K] | Temperature of the surrounding air (in Kelvin). | Hotter air may reduce cooling efficiency and cause overheating.
Process temperature [K] | Temperature inside the machine during operation (in Kelvin). | Higher process temperatures increase stress on components.
Rotational speed [rpm] | How fast a rotating part moves, in revolutions per minute. | Very high or low speeds may lead to stress or poor performance.
Torque [Nm] | Twisting force applied by the machine, in Newton-meters. | Higher torque can increase strain on parts.
Tool wear [min] | How long the tool has been used, measured in minutes. | As wear increases, tools are more likely to fail.
Machine failure | Did the machine fail at this moment? 0 = No, 1 = Yes. | The main target variable for prediction.

## Slide 12
Data dictionary:
TWF (Tool Wear Failure) | Did the machine fail due to worn-out tools? | Shows a specific failure cause.
HDF (Heat Dissipation Failure) | Did the machine fail because heat couldn’t be removed properly? | Related to air vs. process temperature differences.
PWF (Power Failure) | Did the machine fail due to power issues? | Occurs if power output is too high/low.
OSF (Overstrain Failure) | Did the machine fail because of overstrain (too much force on a worn tool)? | Combination of torque + tool wear.
RNF (Random Failure) | A failure that occurs randomly, not explained by conditions. | Mimics real-life unpredictable failures.
Date/Time | Timestamp of when the record was taken. | Enables time-based analysis, trends, and prediction windows.

## Slide 13: Business Question
Core Questions
Diagnostic Questions
Perspective Questions

## Slide 14
Focus :
What happened? Simple KPIs, counts, averages.
Questions
    1. What is the average time between failures for the machines?
    2. Which failures (TWF, HDF, PWF, OSF, RNF) are most common, and which cause the longest downtime?
Core Questions

## Slide 15
Focus :
Relationships, patterns, root causes.
Questions
1. Do certain operating conditions increase the risk of failure?
2. Which parameter is the strongest driver of failures?
3. Are there patterns (after a tool wear threshold) where efficiency drops before failure?
4. Do some machines fail more often than others? Why?
5. Do certain failure types tend to happen together more often than by chance?
Diagnostic Questions

## Slide 16
Focus :
Predictive + recommended actions.
Questions
Can we predict when the next failure is likely to happen?
What is the optimal time to perform maintenance before failures occur?
How many failures could be prevented if maintenance is scheduled proactively (e.g. after 200 min of tool wear)?
What is the probability of failure in the next 24 hours given current conditions?
Are there early warning signals (patterns in torque/air temperature) that could trigger alerts to avoid big breakdowns?
Perspective Questions

## Slide 17: Data Transformation Ideas

## Slide 18
1. Unpivot Failure Modes
2. Power = Torque × Rotational Speed (explicitly calculate it as a column). 3. Temp difference = Process temperature − Air temperature (important for HDF).
4. Tool wear classification Example: Bin tool wear into ranges: Low (<100 min), Medium (100–200), High (>200). Low (<100), Medium (100–200), High (200-240), Critical (>240)”
5. Temp_Diff_Category = Safe (>9), Warning (8.6–9), Risk (<8.6)
6. Power_Category = Safe (3500–9000W), Risk (outside this range)
7. OSF_Category = Safe (<threshold), Risk (≥threshold)
8. Risk_Level = Safe / Medium Risk / High Risk / Failure
9. Utilization Rate= [Power] / 9000
10. Utilization Category :(Under loaded / Optimal / Overloaded). Utilization Rate >0.4 (Under loaded) , <= 0.9(Optimal ) , else (Overloaded)

## Slide 19
Extract features from datetime
11. Hour of day (morning, evening, night).
12. Shift (e.g., divide 24h into 3 shifts: 0–8, 8–16, 16–24).
13. Month / Season.
14. Failure lead time
a target like “failure within the next N hours” instead of “failure now.”

## Slide 20: Insights

## Slide 21
Failure distribution % of machines failed vs not failed Which failure modes are most common
Failure by product type (L/M/H)
Time patterns of failures (day vs night, shift analysis)
Seasonality or environment effects (daily cycle, summer vs winter)
Random failures (RNF) — frequency compared to other failures
Relationship between tool wear and failures (thresholds)
Speed–torque–power relationships (does extreme power correlate with PWF?)
Insights

## Slide 22: Dashboard

## Slide 30: Predictive Maintenance Triggers

## Slide 31
Failure Mode | Threshold | Action
Power Failure | <3.5K or >9K | Stabilize power
Tool Wear | >200 min | Replace tool
OSF (Wear_Torque) | >11K L / 12K M / 13K H | Reduce load
Rotational Speed | <1380 | Check load
Temp Diff | <8.6 | Cooling action
To transition to a proactive maintenance model, alerts should be set at the boundary of the Medium/High Risk zones to enable intervention before failure occurs.

## Slide 32: Recommended Action Plan

## Slide 33
# | Objective | Proposed Action (Based on Prediction) | Key Performance Indicators (KPIs)
1 | Stabilize Power (PWF) | Install Voltage Regulators or UPS Units for critical machines to buffer against sharp spikes (>9K W) and dips (<3.5K W). | Decrease in red zone breaches on the Max Power chart.
2 | Manage Tool Wear (TWF) | Implement an automated Power BI alert that triggers a Tool Replacement Work Order when wear exceeds 200 minutes. | Increase in Mean Time Between Failures (MTBF); 50% reduction in TWF incidents.
3 | Mitigate Overstrain (OSF) | Review operational programs that generate Wear_Torque levels above 11K on Type L products; enforce maximum load limits during peak OSF hours (3 PM/9 PM). | Decrease in OSF incidents for Type L products.
  Immediate Focus (Highest Priority)

## Slide 34
# | Objective | Proposed Action (Based on Report Findings) | Key Performance Indicators (KPIs)
4 | Improve Operating Environment | Install supplementary cooling in the machine area, specifically ahead of the high-risk season (September to December). | Decrease in failure correlation with ambient air temperature in Q4.
5 | Review Shift Procedures | Conduct an audit of the operations, training, and supervision during Shift 3 and the Night period to identify operational gaps contributing to high failure rates. | Decrease in Shift 3's contribution to total failure incidents.
  2. Mid-Term / Environment & Process Focus

## Slide 35: Project Impact

## Slide 36
Clear visibility on root causes (90% downtime explained)
Automated monitoring instead of manual analysis
Predictive thresholds to prevent failures
Expected improvement in MTBF
Early warnings = lower cost of maintenance

## Slide 37: Thanks!
Do you have any questions?